## Slide 1
Indoor Localization system using Time of Flight in UWB spectrum
Anirban Ghosh
Albert Davies
Tejus Siddagangaiah

## Slide 2
Objective
Compute a mobile node’s position in 3 Dimension in an indoor setting

## Slide 3
Application and Use Cases
Indoor Localization systems can be developed and applied to any large venue: Shopping Malls, Airports, Universities, etc.
Indoor Localization systems can be used to provide directions, provide relevant advertisement, raise requests for help, asset tracking etc.
Similar localization systems can also be used in remote environments like coal mines to track coal miners
Image source: Google

## Slide 4
Approaches to achieve localization
BLE
Ultrasound
WiFi
UWB
Zigbee
Cameras
LEDs

## Slide 5
System Architecture and Design
Admin System
PC/Laptop
Mobile Node
Anchor Node - I
Anchor Node - II
Anchor Node - III
Aruduino Uno Wifi
Atmega 328
Network Processor
Peripherals and Power Management
Decawave
DW1000 Module
SPI
Arduino Uno Wifi
Atmega 328
Network Processor
Peripherals and Power Management
Decawave
DW1000 Module
SPI
Arduino Uno Wifi
Atmega 328
Network Processor
Peripherals and Power Management
Decawave
DW1000 Module
SPI
Arduino Uno Wifi
Atmega 328
Network Processor
Peripherals and Power Management
Decawave
DW1000 Module
SPI
WiFi

## Slide 6
System Diagram of a Node
Arduino Uno Wifi
Atmega 328
Network Processor
Peripherals and Power Management
Decawave
DW1000 Module
SPI

## Slide 7
DWM1000 Module
IEEE802.15.4-2011 UWB Compliant (Operates from 3.5 – 6.5 GHz)
Locates objects to a precision of 10cm indoors
Up to 290m LOS
Highly immune to multipath fading
Factory trimmed
Integrated Antenna

## Slide 8
Localization schemes
DWM1000 Modules can be used in two modes:
  2 – way ranging (Time of flight)
  Time Difference of Arrival(TDOA)

## Slide 9
MID Semester Presentation
Achieved distance ranging in 1 dimension with visual front-end

## Slide 10
DWM1000 Distance Ranging Accuracy
Not accurate for short distances out of the box.
Chart: Percentage error vs Distance
| 0.1 | 0.2 | 0.5 | 1.0 | 2.0 | 3.0 | 5.0 | 10.0
Column D | 320 | 230 | 126 | 76 | 57.5 | 33.3333 | 19 | 9.8

## Slide 11
Current State of Project
Localization working!!
Localization working!!

## Slide 12
But...
Increase accuracy
Constrain co-ordinate space
Sensitive to Anchor Placement
Integrate WiFi

## Slide 13
Timeline
Week | Milestone | Status
Mar 27-31 | Basic Arduino Code test, Solder 2x DW1000 modules, breadboard prototyping, Py interface | Done
Apr 3-7 | Mid term demo. Level shifters interface, DW1000 baseboards arrive, Perf board bring up | Done
Apr 10-14 | Develop TOF code with 5 DW1000 modules working at once. | Done
Apr 17-21 | Change library for robust multi-anchor network connectivity and addressing | Done
Apr 24-28 | Test TOF Code with 4 anchor+1 tag. Accuracy measurements, integrating solver code with python interface code and GUI extension | Done
May 1-5 | Prep for final demos, code and H/W cleanup, calibrations, WiFi Integration | Pending

## Slide 14
Final Demonstration
Final demonstration: Use multiple anchor nodes whose locations are pre-determined to track the mobile node in the same environment. Display the movement of the mobile node on a GUI(using a PC application) in real time

## Slide 15
Questions?

## Slide 16
Tag to Admin via WiFi
TAG
ANCHOR 0
ANCHOR 1
ANCHOR 2
POLL
POLL_ACK
RANGE_INIT
RANGE
time

## Slide 17
Z - axis
x - axis
y- axis
ANCHOR – 0 (0, 0, 0)
ANCHOR – 1 (0, 0, 2.34)
ANCHOR – 2 (4.63, 0, 2.34)
ANCHOR – 3 (0, 3.6, 2,34)